## Slide 1: IF2130/II2130 – Organisasi dan Arsitektur Komputer sumber: Greg Kesden, CMU 15-213, 2012
Achmad Imam Kistijantoro
Anggrahita Bayu Sasmita
Yudistira Dwi Wardhana Asnar
Rahmat Mulyawan
Infall Syafalni
Representasi Informasi – IEEE Floating Point Standard

## Slide 2: IEEE Floating Point
IEEE Standard 754
  Established in 1985 as uniform standard for floating point arithmetic
    Before that, many idiosyncratic formats
  Supported by all major CPUs
Driven by numerical concerns
  Nice standards for rounding, overflow, underflow
  Hard to make fast in hardware
    Numerical analysts predominated over hardware designers in defining standard

## Slide 3: Floating Point Representation
Numerical Form: (–1)s M 2E
  Sign bit s determines whether number is negative or positive
  Significand M normally a fractional value in range [1.0,2.0).
  Exponent E weights value by power of two
Encoding
  MSB s is sign bit s
  exp field encodes E (but is not equal to E)
  frac field encodes M (but is not equal to M)
s | exp | frac

## Slide 4: Precision options
Single precision: 32 bits
Double precision: 64 bits
Extended precision: 80 bits (Intel only)
s | exp | frac
1 | 8-bits | 23-bits
s | exp | frac
1 | 11-bits | 52-bits
s | exp | frac
1 | 15-bits | 63 or 64-bits

## Slide 5: End of Segment