## Slide 1: IF2130/II2130 – Organisasi dan Arsitektur Komputer sumber: Greg Kesden, CMU 15-213, 2012
Achmad Imam Kistijantoro
Anggrahita Bayu Sasmita
Yudistira Dwi Wardhana Asnar
Rahmat Mulyawan
Infall Syafalni
Representasi Informasi – Integers Expanding & Truncating

## Slide 2: Sign Extension
Task:
  Given w-bit signed integer x
  Convert it to w+k-bit integer with same value
Rule:
  Make k copies of sign bit:
  X  = xw–1 ,…, xw–1 , xw–1 , xw–2 ,…, x0
k copies of MSB
• • •
X
X 
• • •
• • •
• • •
w
w
k

## Slide 3: Sign Extension Example
Converting from smaller to larger integer data type
C automatically performs sign extension
short int x = 15213;
int ix = (int) x;
short int y = -15213;
int iy = (int) y;
Decimal
Hex
Binary
x
15213
3B 6D
00111011 01101101
ix
15213
00 00 3B 6D
00000000 00000000 00111011 01101101
y
-15213
C4 93
11000100 10010011
iy
-15213
FF FF C4 93
11111111 11111111 11000100 10010011

## Slide 4: Summary: Expanding, Truncating: Basic Rules
Expanding (e.g., short int to int)
  Unsigned: zeros added
  Signed: sign extension
  Both yield expected result
Truncating (e.g., unsigned to unsigned short)
  Unsigned/signed: bits are truncated
  Result reinterpreted
  Unsigned: mod operation
  Signed: similar to mod
  For small numbers yields expected behaviour

## Slide 5: End of Segment