## Slide 1: IF2130/II2130 – Organisasi dan Arsitektur Komputer sumber: Greg Kesden, CMU 15-213, 2012
Achmad Imam Kistijantoro
Anggrahita Bayu Sasmita
Yudistira Dwi Wardhana Asnar
Rahmat Mulyawan
Infall Syafalni
Representasi Informasi – Multiplications

## Slide 2: Multiplication
Goal: Computing Product of w-bit numbers x, y
  Either signed or unsigned
But, exact results can be bigger than w bits
  Unsigned: up to 2w bits
    Result range: 0 ≤ x * y ≤ (2w – 1) 2 = 22w – 2w+1 + 1
  Two’s complement min (negative): Up to 2w-1 bits
    Result range: x * y ≥ (–2w–1)*(2w–1–1) = –22w–2 + 2w–1
  Two’s complement max (positive): Up to 2w bits, but only for (TMinw)2
    Result range: x * y ≤ (–2w–1) 2 = 22w–2
So, maintaining exact results…
  would need to keep expanding word size with each product computed
  is done in software, if needed
    e.g., by “arbitrary precision” arithmetic packages

## Slide 3: Unsigned Multiplication in C
Standard Multiplication Function
  Ignores high order w bits
Implements Modular Arithmetic
  UMultw(u , v) = u · v mod 2w
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: 2*w bits
Operands: w bits
Discard w bits: w bits
UMultw(u , v)
• • •

## Slide 4: Signed Multiplication in C
Standard Multiplication Function
  Ignores high order w bits
  Some of which are different for signed vs. unsigned multiplication
  Lower bits are the same
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: 2*w bits
Operands: w bits
Discard w bits: w bits
TMultw(u , v)
• • •

## Slide 5: Power-of-2 Multiply with Shift
Operation
  u << k gives u * 2k
  Both signed and unsigned
Examples
  u << 3 == u * 8
  u << 5 - u << 3 == u * 24
  Most machines shift and add faster than multiply
    Compiler generates this code automatically
• • •
0
0
1
0
0
0
•••
u
2k
*
u · 2k
True Product: w+k bits
Operands: w bits
Discard k bits: w bits
UMultw(u , 2k)
•••
k
• • •
0
0
0
•••
TMultw(u , 2k)
0
0
0
•••
•••

## Slide 6: Unsigned Power-of-2 Divide with Shift
Quotient of Unsigned by Power of 2
  u >> k gives  u / 2k 
  Uses logical shift
0
0
1
0
0
0
•••
u
2k
/
u / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
0
0
•••
•••
 u / 2k 
•••
Result:
.
Binary Point
0
0
0
0
•••
0

## Slide 7: Signed Power-of-2 Divide with Shift
Quotient of Signed by Power of 2
  x >> k gives  x / 2k 
  Uses arithmetic shift
  Rounds wrong direction when u < 0
0
0
1
0
0
0
•••
x
2k
/
x / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
•••
•••
RoundDown(x / 2k)
•••
Result:
.
Binary Point
0
•••

## Slide 8: Correct Power-of-2 Divide
Quotient of Negative Number by Power of 2
  Want  x / 2k  (Round Toward 0)
  Compute as  (x+2k-1)/ 2k 
    In C: (x + (1<<k)-1) >> k
    Biases dividend toward 0
Case 1: No rounding
Divisor:
Dividend:
0
0
1
0
0
0
•••
u
2k
/
 u / 2k 
•••
k
1
•••
0
0
0
•••
1
•••
0
1
1
•••
.
Binary Point
1
0
0
0
1
1
1
•••
+2k –1
•••
1
1
1
•••
1
•••
1
1
1
•••
    Biasing has no effect

## Slide 9: Correct Power-of-2 Divide (Cont.)
Divisor:
Dividend:
Case 2: Rounding
0
0
1
0
0
0
•••
x
2k
/
 x / 2k 
•••
k
1
•••
•••
1
•••
0
1
1
•••
.
Binary Point
1
0
0
0
1
1
1
•••
+2k –1
•••
1
•••
•••
    Biasing adds 1 to final result
•••
Incremented by 1
Incremented by 1

## Slide 10: Arithmetic: Basic Rules
Addition:
  Unsigned/signed: Normal addition followed by truncate, same operation on bit level
  Unsigned: addition mod 2w
    Mathematical addition + possible subtraction of 2w
  Signed: modified addition mod 2w (result in proper range)
    Mathematical addition + possible addition or subtraction of 2w
Multiplication:
  Unsigned/signed: Normal multiplication followed by truncate, same operation on bit level
  Unsigned: multiplication mod 2w
  Signed: modified multiplication mod 2w (result in proper range)

## Slide 11: Why Should I Use Unsigned?
Don’t Use Just Because Number Nonnegative
  Easy to make mistakes
    unsigned i;
    for (i = cnt-2; i >= 0; i--)
    a[i] += a[i+1];
  Can be very subtle
    #define DELTA sizeof(int)
    int i;
    for (i = CNT; i-DELTA >= 0; i-= DELTA)
    . . .
Do Use When Performing Modular Arithmetic
  Multiprecision arithmetic
Do Use When Using Bits to Represent Sets
  Logical right shift, no sign extension

## Slide 12: End of Segment