## Slide 1: IF2130/II2130 – Organisasi dan Arsitektur Komputer sumber: Greg Kesden, CMU 15-213, 2012
Achmad Imam Kistijantoro
Anggrahita Bayu Sasmita
Yudistira Dwi Wardhana Asnar
Rahmat Mulyawan
Infall Syafalni
Representasi Informasi – Floating Point: Fractional Binary Number

## Slide 2: Fractional binary numbers
What is 1011.1012?

## Slide 3: Fractional Binary Numbers
2i
2i-1
4
2
1
1/2
1/4
1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
• • •
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
• • •
Notes: Latex source for equation: \sum_{k=-j}^i b_k \times 2^k

## Slide 4: Fractional Binary Numbers: Examples
Value Representation
5 3/4 101.112
2 7/8 010.1112
1 7/16 001.01112
Observations
  Divide by 2 by shifting right (unsigned)
  Multiply by 2 by shifting left
  Numbers of form 0.111111…2 are just below 1.0
    1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0
    Use notation 1.0 – ε

## Slide 5: Representable Numbers
Limitation #1
  Can only exactly represent numbers of the form x/2k
    Other rational numbers have repeating bit representations
  Value Representation
    1/3 0.0101010101[01]…2
    1/5 0.001100110011[0011]…2
    1/10 0.0001100110011[0011]…2
Limitation #2
  Just one setting of decimal point within the w bits
    Limited range of numbers (very small values? very large?)

## Slide 6: End of Segment